## Slide 1: The History of Masonry
Masonry construction dates back 8000 years
Some of the world’s most significant architectural achievements have been built with masonry

## Slide 4: History of Mortars
The first mortars were made from mud or clay. These materials were used because of availability and low cost
It was discovered that limestone, when burnt and combined with water, produced a material that would harden with age.
The Romans created hydraulic mortars that contained lime and a pozzolan such as brick dust or volcanic ash

## Slide 5: History of Mortars
Joseph Aspdin, an English mason/builder patented a material called Portland cement in 1824
Portland cement combined with lime provided an excellent balance between strength and workability.
The addition of Portland cement to lime mortars increased the speed of the construction process for masonry building due to faster strength development

## Slide 6: ASTM C-270
Specification for mortars:
  Proportion
  Properties

## Slide 7: WHAT IS THE ROLE OF MORTAR? Holds units together or hold units apart?

## Slide 8: WHAT ELSE CAN GOOD MORTAR DO? It accommodates for uneven units!
Mortar can fill non-uniform spaces between units to result in a plumb and level masonry wall.

## Slide 9
Masonry Materials Basics
WHAT ABOUT THE WEATHER?
Water Penetration Resistance
Rain
Good mortar bonds the units together and proper tooling creates a water resistant masonry assemblage.

## Slide 10
WHAT’S IN GOOD “MUD”?
  Cement
  Lime
  Sand
  Water
  Admixtures

## Slide 11
Masonry Materials Basics
CEMENT: Provides structural performance
  Cement
  Lime
  Sand
  Water
  Admixtures
Portland Cement (C 150)
Masonry Cement (C 91), or
Mortar Cement (C 1329)
Compressive Strength
Early Setting
Bond Strength
Durability
Shrinkage

## Slide 12
Masonry Materials Basics
LIME: Mortar’s secret weapon!
  Cement
  Lime
  Sand
  Water
  Admixtures
Hydrated Lime (C 207)
Workability
Water Retentivity
Late Strength
Autogenous Healing

## Slide 13
Masonry Materials Basics
MASONRY SAND: The backbone of mortar!
  Cement
  Lime
  Sand
  Water
  Admixtures
Masonry Sand (C 144)
Bulk and Body
Yield
Strength
Shrinkage Resistance

## Slide 14
MORTAR SELECTION: Based on two desired properties
1. Plastic Mortar 2. Hardened Mortar – Workability – Bond strength and intimacy – Water retentivity – Compressive strength “board life” – Durability and resistance – Stiffening characteristic
Other factors: Climate, seismicity, water penetration, shrinkage or color.

## Slide 15
WHAT ARE THE ASTM C270 MORTAR DESIGNATIONS AND HOW WERE THEY DETERMINED?
M a S o N w O r K

## Slide 16: MORTAR’S RECIPE SPECIFICATION! ASTM C 270 Proportion Specification: Mortar by volume

## Slide 17: Mortar by Proportion

## Slide 18: Type S Mortar (By Proportion) Type S is the most common mortar is Arizona
Portland Cement / Lime Mortar
94# Bag Portland Cement = 1 cubic foot
50# Bag of Lime = 1 cubic foot
7 square shovels of Sand = 1 cubic foot (+ or -)
2 Portland Cement + 1 Lime = 3 C.F. Cementitious
3 C.F. X 2 ¼ to 3 C.F. Sand = 6 ¾ to 9 C.F. Sand
6 ¾ to 9 C.F. = 47 to 63 Shovels Damp Loose Sand
Most commonly used is 56 shovels of sand
This makes a “full mixer” of mortar

## Slide 19: Mortar Property Specification

## Slide 20: Two Ways to Make Mortar
Masonry Materials Basics
1. Field mixed 2. Preblended

## Slide 21: Field Mixed Mortar
Masonry Materials Basics
Heavy lifting
Twisting and turning

## Slide 22
Masonry Materials Basics
FIELD MIX MORTAR QUALITY(?)
Is 20 shovels enough…
And, how much color?

## Slide 23: Amerimix Factory
Masonry Materials Basics
SUPERLITE

## Slide 25: It’s Contamination Free
Masonry Materials Basics
Packaged completely dry and sealed tight!
What’s in the sand?
Soluble salts
Dirt mixed into the sand

## Slide 26: Grout
What is Grout?
    A high slump concrete used to fill voids in the masonry assemblage to bind everything together.
Grout is specified either by:
  Proportions contained in C-476, or
  Strength (property) requirements
If compressive strength is not specified, minimum strength is 2000 psi at 28 days according to ASTM C 1019

## Slide 31
Proper Work Attire and PPE
Wear Close-Fitting
Clothing.
Wear Gloves When
Working With Wet
Mortar.
Belt Should
be Above Hips.
Ensure Pants Do Not Sag (2-Inch Maximum Inseam).
Always Wear a Hard Hat.
Wear Long-Sleeved
Shirts to Give Extra
Protection if Skin
is Sensitive (Minimum 4-Inch Sleeve).
Wear High-Visibility Vest
(Where Required).
Wear Pants Over
Boots to Avoid
Getting Mortar
on Legs or Feet.
Keep Gloves and Clothing as Dry as Possible.
Wear Goggles When
Cutting or Grinding.
Notes: Discuss with trainees the importance of each aspect of appropriate clothing and equipment for a mason.